## Slide 1
LVAE for Thermoelastic 2D Topology Optimisation
Reducing the train/val NMSE gap · Exploring the latent dimensionality sweet spot
Thomas Casartelli · April 2026 · EngiOpt / ETH Zürich
EngiOpt · ETH Zürich · IDEAL Lab

## Slide 2
Problem Setting
Thermoelastic 2D topology optimisation · IDEALLab/thermoelastic_2d_v1
The dataset
• 14 400 train / 1 800 val / 1 800 test (18 000 total, v1)
• Each design: 64×64 float32 density field in [0,1] — SIMP-relaxed binary topology.
• Goal: minimise structural + thermal compliance under a volume fraction constraint.
• Each sample has unique, randomly generated boundary conditions:
volfrac ∈ [0.2, 0.5] · weight ∈ [0,1] · load/fix/heatsink positions
→ High inter-sample diversity makes latent generalisation hard but ensures rich Var(data).
The LVAE
• Autoencoder that minimises the geometric mean of latent std — compresses unused dimensions.
• Volume pressure gated on NMSE ≤ τ, preventing compression before reconstruction is acceptable. NMSE = MSE / Var(data).
• Plummet pruning (from epoch 500): detects and removes dimensions with sharply collapsed std.
• Three variants tested:
Vanilla LVAE — rec loss only
Constrained LVAE — one-sided NMSE constraint
Constrained PLVAE — NMSE + performance predictor
→ Key research question: what is the right latent dimensionality and threshold τ for this dataset?

## Slide 3
The Core Problem: Train / Val NMSE Gap
The encoder memorises training data — volume pressure activates prematurely
Observed numbers
Baseline BN encoder (ep 83, stopped early)
Val NMSE 0.171 / Vol not activated
GN + SN encoder (ep 2088)
Train NMSE 0.048 ✓ / Val NMSE 0.197 ✗
Gap = 4.1× / Vol never activated
Both with τ = 0.05 (default threshold)
14 400 training samples: overfitting
is NOT a small-dataset effect.
It is a genuine encoder capacity issue.
Root cause
• Encoder maps training samples to tight, precise latent codes. For val samples, codes are noisier and less well-separated.
• BN → GN swap eliminated train/eval statistics mismatch but left the gap unchanged: the problem is encoder capacity, not normalisation.
• With τ=0.05, train NMSE satisfies the constraint while val NMSE stays at ~0.20. Volume activates on overfitting data → compresses a space that hasn't generalised.
Key insight from τ sweep
• τ is the most sensitive hyperparameter. Too low → vol never activates. Too high → over-compression.
★ τ = 0.20 is the sweet spot: vol activates reliably, pruning stays light, val NMSE minimised at 0.182.
Strategies tested
1. GN + SN encoder
2. Latent noise σ=0.1
3. Val-gate τ=0.05
4. τ sweep (8 values)
5. τ=0.20 + noise ← NEW

## Slide 4
Strategy 1 — GN + Spectral Norm Encoder [DONE]
Stabilise encoder output distribution · necessary but insufficient
WHY & HOW
• BatchNorm computes running statistics on training data; at eval time these create a distribution shift in z. GroupNorm normalises using each sample's own channel statistics — no train/eval gap.
• Spectral Normalisation re-scales each weight matrix so its largest singular value ≤ 1. Encoder becomes 1-Lipschitz: small input changes → equally small or smaller changes in z.
→ GN removes the artefact; SN bounds sensitivity. Together: a more stable and predictable latent representation.
Results
cLVAE ep 2088: train 0.048 ✓ / val 0.197 ✗ gap 4.1× / 100/100 dims
LVAE ep 2050: train rec 0.006 / val rec 0.034 gap 5.8× / 90/100 dims
cPLVAE ep 2078: NMSE_rec 0.087 / val 0.304 gap 3.5× / vol never active
✗ Verdict: BN was NOT the root cause. Gap persists with GN.
What this means
• The gap is intrinsic to the encoder's expressive capacity, not to normalisation artifacts.
• With 14.4k diverse training samples, the encoder learns to map each sample to a tightly clustered latent region — but this precision doesn't transfer to val samples.
• GN + SN is still correct and kept as the encoder standard: it eliminates one source of error and bounds sensitivity. All subsequent experiments use it.
→ Next needed: regularisation that directly constrains encoder overfitting, OR finding the right threshold τ so volume pressure activates at the right time.

## Slide 5
Strategy 4 — NMSE Threshold Sweep (τ ∈ {0.01 … 0.70}) [DONE]
Finding the dimensionality sweet spot · 8 values · constrained LVAE
τ | Train NMSE | Val NMSE | Active dims | Vol active | Regime
0.01 | 0.035 | 0.211 | 100/100 | ✗ | Unreachable
0.03 | 0.035 | 0.211 | 100/100 | ✗ | Unreachable
0.05 | 0.067 | 0.198 | 100/100 | ✗ | Borderline
0.10 | 0.077 | 0.191 | 100/100 | ✓ | Compression
0.20 | 0.088 | 0.182 | 97/100 | ✓ | ★ SWEET SPOT
0.30 | 0.117 | 0.239 | 43/100 | ✓ | Over-compress
0.50 | 0.126 | 0.251 | 45/100 | ✓ | Over-compress
0.70 | 0.131 | 0.317 | 14/100 | ✓ | Over-compress
What the sweep shows
U-shape:Val NMSE forms a U as τ increases.
Low τ (0.01–0.05): vol never activates. Encoder trains freely → memorises.
τ=0.20 SWEET SPOT. Vol activates, light pruning (97 dims), val NMSE minimised at 0.182.
High τ (≥0.30): over-compression. Model forced to squeeze too much into too few dims. Val NMSE climbs back up despite pruning (43 → 14 active dims).
→ τ is the most impactful hyperparameter found so far.
→ Best val NMSE overall: 0.182 at τ=0.20.

## Slide 7
Strategy 2 — Latent Noise Injection σ=0.1 [DONE]
Forcing decoder robustness against imprecise codes · τ=0.05 in these runs
Mechanism
• Gaussian noise (σ=0.1) added to each active latent dim before decoding — training only.
• Decoder learns neighbourhood robustness: codes near the encoder output should reconstruct correctly.
• Prevents train rec from collapsing to near-zero — model cannot memorise exact codes.
• Clean z used for volume pressure and pruning statistics — compression driven by true distribution.
Analogy: Dropout in the latent space. Prevents decoder from relying on exact codes.
Results by variant (ep ~2050, τ=0.05)
Model | Train | Val NMSE | Gap | Dims | Vol
Vanilla LVAE | — | rec 0.034 | 5.3× | 69/100 | Yes
cLVAE ★ | 0.050 | 0.188 | 3.8× | 100/100 | Yes
cPLVAE | 0.091 | 0.311 | 3.4× | 100/100 | No
Interpretation
✓ cLVAE: val NMSE 0.188 — improvement over GN baseline (0.197). Vol activated. Gap 4.1× → 3.8×.
✓ Vanilla LVAE: only run achieving real pruning at τ=0.05 (69/100 dims). Noise prevents catastrophic memorisation (train rec stays at 0.006 vs 0.0004 baseline).
~ cPLVAE: rec_violated throughout (0.091 > 0.05 threshold). Vol never activated. Joint constraint too tight.
✗ None reached val NMSE < 0.10. Gap persists at 3–5×.
→ Noise helps but τ=0.05 limits compression. Next: combine noise with τ=0.20 (the sweet spot).

## Slide 8
Strategy 3 — Validation-Gated Volume Loss [DONE — Negative Result]
Gate volume on val NMSE < τ · gate never opened · gap increased
What happened
✗ val_nmse_ok = 0 for the entire run (all 3 variants). Gate never opened.
LVAE: train 0.029 / val 0.226 gap 7.8× dims 100/100
cLVAE: train 0.029 / val 0.226 gap 7.9× dims 100/100
cPLVAE: train 0.080 / val 0.317 gap 4.0× dims 100/100
✗ Val NMSE always ~0.23 — the threshold 0.05 is completely unreachable when the gate is blocking compression.
✗ Gap INCREASED vs GN baseline: 7.8× vs 4.1%. The val gate made things WORSE.
Why removing volume pressure backfires
• Volume pressure is not only a compression mechanism — it is also a regulariser. By forcing the encoder to map designs into a compact manifold, it limits overfitting capacity.
• Removing volume pressure (via the gate) gives the encoder full freedom to use all 100 latent dimensions. More capacity → more memorisation → larger gap.
→ Result: train rec drops to 0.029 (worse than with vol pressure!) while val NMSE climbs to 0.226.
The fix:Gate threshold must be reachable. With τ_gate=0.05 and val NMSE always ≥ 0.20, the gate is equivalent to permanently disabling the LVAE.
→ Better approach: use τ_gate=0.25 (reachable) OR gate on a relative criterion (val/train ratio < 2×) rather than an absolute threshold.

## Slide 9
Complete Results Table
All experiments · constrained LVAE unless noted · ordered by val NMSE
Method | τ | Noise σ | Train NMSE | Val NMSE | Gap | Active dims | Vol | Status
Baseline BN (ep 83 ⚠) | 0.05 | — | 0.108 | 0.171 | — | — | No | Done
τ sweep τ=0.20 ★ best | 0.20 | — | 0.088 | 0.182 | — | 97/100 | Yes | Done
GN+noise cLVAE | 0.05 | 0.1 | 0.050 | 0.188 | 3.8× | 100/100 | Yes | Done
τ sweep τ=0.10 | 0.10 | — | 0.077 | 0.191 | — | 100/100 | Yes | Done
GN encoder cLVAE (baseline) | 0.05 | — | 0.048 | 0.197 | 4.1× | 100/100 | No | Done
τ sweep τ=0.05 | 0.05 | — | 0.067 | 0.198 | — | 100/100 | No | Done
GN+noise vanilla LVAE | 0.05 | 0.1 | — | 0.034* | 5.3× | 69/100 | Yes | Done
Val gate cLVAE | 0.05 | — | 0.029 | 0.226 | 7.9× | 100/100 | No | Done ✗
Val gate vanilla LVAE | 0.05 | — | 0.029 | 0.226 | 7.8× | 100/100 | No | Done ✗
τ sweep τ=0.30 | 0.30 | — | 0.117 | 0.239 | — | 43/100 | Yes | Done
cPLVAE GN+noise | 0.05 | 0.1 | 0.091† | 0.311 | 3.4× | 100/100 | No | Done
Val gate cPLVAE | 0.05 | — | 0.080† | 0.317 | 4.0× | 100/100 | No | Done ✗
τ sweep τ=0.50 | 0.50 | — | 0.126 | 0.251 | — | 45/100 | Yes | Done
τ sweep τ=0.70 | 0.70 | — | 0.131 | 0.317 | — | 14/100 | Yes | Done
τ=0.20 + noise ← NEW | 0.20 | 0.1 | — | — | — | — | — | Running
* val rec (raw) not NMSE · † rec_violated · ★ best val NMSE · ⚠ ep 83 stopped early

## Slide 10
Key Findings
What the experiments reveal about LVAE on thermoelastic2D
What worked
✓ τ = 0.20 is the sweet spot. Best val NMSE = 0.182, 97/100 active dims, vol activated. τ is more impactful than encoder architecture or noise.
✓ Latent noise (σ=0.1) at τ=0.05 reduces gap from 4.1× → 3.8× and gives val NMSE 0.188. Decoder robustness improves generalisation.
✓ Vanilla LVAE + noise: only run with real pruning at τ=0.05 (69/100 dims). Noise prevents catastrophic memorisation.
✓ GN + SN encoder: correct choice regardless. Eliminates BN stats mismatch and bounds Lipschitz constant.
✓ Sweep answered supervisor question 1: dimensionality sweet spot is ~97 dims at τ=0.20.
What did not work / key insights
✗ Val gate (absolute τ=0.05): gate never opened. Removing vol pressure increased the gap (7.8× vs 4.1×). Vol pressure IS a regulariser.
✗ cPLVAE: joint rec+perf constraint at τ=0.05 is too tight. rec_violated throughout all cPLVAE runs. Needs threshold relaxation.
✗ No method achieved val NMSE < 0.10. The 0.05 target on val remains distant.
→ Key insight: over-compression (τ≥0.30) hurts val NMSE as much as under-compression (τ≤0.03). The U-shape is the central finding.
→ Best unexplored combination: τ=0.20 + noise σ=0.1. Currently running.

## Slide 11
Next Steps — Aligned with Supervisor Suggestions
Prioritised roadmap based on experimental findings
RUNNING · τ=0.20 + noise σ=0.1 (best two strategies combined)
Should yield val NMSE ≤ 0.182 with more aggressive pruning. Supervisor question 1 partly answered; this validates whether the two improvements are additive.
Dataset complexity vs. dimensionality (supervisor priority)
Subset by weight=1.0 (structural only) vs weight=0.0 (thermal only): how many dims does each sub-problem need? Subset by volfrac range. This directly addresses 'explore LVAE on subsets' and 'relationship between GLVAE dimension and dataset complexity'.
Condition-aware decoder (supervisor: 'condition-aware decoder so latent space doesn't need to double up')
Concatenate conditions (volfrac, weight, BC hash) to the decoder input. Latent z encodes only topology structure — not conditions. Should reduce required active dims and improve generalisation.
Val gate with reachable threshold (τ_gate = 0.20–0.25)
The absolute τ=0.05 gate is permanently closed. Gate on τ_gate=0.20 (reachable) OR on relative criterion val/train ratio < 2×. Combines benefits of compression guard with actual vol pressure.
Visualisation study (supervisor: 'overall visualisations of different LVAE variants')
Compare LVAE variants on: interpolation quality, unconditional sampling, latent clustering by condition (weight, volfrac), placement of unseen conditions.

## Slide 12
Summary
Progress, key numbers, and direction
Completed experiments
✓ GN + SN encoder — all 3 variants
✓ Latent noise σ=0.1 — all 3 variants
✓ Val gate τ=0.05 — all 3 variants
✓ τ sweep: 8 values (0.01–0.70)
⟳ τ=0.20 + noise — running
✓ Dataset confirmed: 14.4k train / 1.8k val+test
✓ All tracked on WandB (spectral_norm_encoder)
Best results
★ Val NMSE 0.182
τ=0.20 sweep / 97 active dims
Val NMSE 0.188
cLVAE + noise / τ=0.05
69/100 active dims
Vanilla LVAE + noise (only pruned run)
Baseline BN: val NMSE 0.171 (ep 83, early stopped — not a fair comparison)
Target: val NMSE < 0.05
Remaining gap: ~3.6–4×
Conclusions
• τ is the dominant hyperparameter — more impactful than encoder type or noise.
• Volume pressure is both a compression mechanism AND a regulariser. Disabling it (val gate) increases overfitting.
• The U-shape (unreachable → sweet spot → over-compress) is the central finding. It directly answers the supervisor's 'dimensionality sweet spot' question.
• Noise injection and τ tuning are complementary and unexplored in combination — that is the running experiment.
• Next frontier: dataset subsets by condition (weight, volfrac) to understand how dataset complexity drives the required latent dimensionality.